## Slide 1: Plasma Diagnostic Techniques Lecture 17: Absorption spectroscopy
York Plasma Institute

## Slide 2
Recap: Radiative transfer

## Slide 3
Optical transitions: photon absorption
Photon absorption
  The Einstein coefficient Bki describes the transition probability for photon absorption from a lower energy level k to a higher energy level i.
The discrete (line absorption) energy Eki of the corresponding photon is directly related to the frequency nki (wavelength lki) of the absorbed photon.
The number of absorbed photons per unit volume and time is given by:
  k
  i

## Slide 4
Recap: Line profiles

## Slide 5
Spectral line profiles φ(λ)
  Natural line broadening
  Doppler broadening
    particle motion
  Pressure broadening
    particle collisions
  Others, e.g. Stark broadening, instrumental broadening

## Slide 6
Principles of Absorption Spectroscopy

## Slide 7
  Use light for excitation!
  Therefore, AS is
    Direct (no model needed, in contrast to emission based techniques)
    Relatively easy to implement
    Invasive (but not too much)
    No spatial resolution
  Light source
  Detector
  Plasma
Principles of AS

## Slide 8
  … + 2 signals
    IP Correction for plasma emission
    I0 Background correction
  x
  I(x)
  IL
  2 Signals…
    IL Intensity of light source
    IP,L Intensity after light passed medium
  IL
  IP,L
  Exponential decay!
  λ
Beer-Lambert-Law
  Define transmission
  A absorbance
  IP

## Slide 9
  n species density (lower energy level)
  l absorption length
  σ(λ) absorption cross section
  α absorption coefficient
  How to get densities? Let’s have a look at the absorbance
  σ is a measure for the probability of the transition
Beer-Lambert-Law
  k
  i

## Slide 10
Absorption cross sections
  O3 absorption cross sections

## Slide 11
  α is a measure for the probability of the transition and usually contains the normalised line profile φ(λ)
  Integration over line-profile necessary
AS and line profiles

## Slide 12
  Simplest case: Electronic transitions in atoms
  Atomic oxygen
AS on atomic species
Niemi et al., APL, 2013
  Atmospheric pressure plasma:
  O(2p4 3P2)
  O (3s 3S1)
  Ground state
  130 nm

## Slide 13
  Single line profile with Doppler and pressured broadened line
  Vacuum Ultra-Violet AS on atomic oxygen
AS on atomic species
  Simplest case: Electronic transitions in atoms
  Atomic oxygen
  O(2p4 3P2)
  O (3s 3S1)
  Ground state
  130 nm

## Slide 14
  Electronic, rotational and vibrational transitions
AS on molecules
  Vibration:
  e.g. OH
  e.g. H2O
  e.g. CO2
  Symmetric stretch
  Asymmetric stretch
  Bending
  Linear molecules
  Non-linear molecules
  𝜆 in infra-red (IR) spectral range
  ν wavenumber (in cm-1)
  The energy required for vibr. excitation depends on mode of vibration, bond strength, and mass of atoms. Imagine bond as a spring:

## Slide 15
  IR AS on CO2: CO2(v”) → CO2 (v’)
AS on molecules – IR spectroscopy
  To detect molecules with IR-spectroscopy, dipole moment has to change!
  Not detectable (CO2 sym. stretch)
  Detectable (CO2 asym. stretch)
  +
  -
  +
  -
  -
  Ar + CO2
  +
  -

## Slide 16
  Electronic, rotational and vibrational transitions
AS on molecules
  Rotation:
  Rotational quantum numbers
  Vibration:
  e.g. OH
  e.g. H2O
  e.g. CO2
  Symmetric stretch
  Asymmetric stretch
  Bending
  Vibrational quantum numbers
  Linear molecules
  Non-linear molecules

## Slide 17
  Rotational transitions in molecules
  UV AS on hydroxyl radicals (OH)
  OH(X,v”=0) → OH(A,v’=0)
  Multiple lines, instrumental broadening dominant
AS on molecules - UV spectroscopy
  i,k are different rotational levels!

## Slide 18
  In principle AS can be used to detect any species of interest, as long as
    cross sections are known
    species densities are not too high/low
    desired wavelength is “accessible”
AS summary

## Slide 19
Apparatus for absorption Spectroscopy

## Slide 20
  3 components:
  Light source (tunable or broad-band)
    LED
    Diode lasers
    Plasma lamps
    Synchrotron radiation
  Optics (beam “shaping”, e.g. focussing or collimating)
  Detector (coupled with spectrometer)
    Photodiode arrays
    CCD chips
AS setup

## Slide 21: Experimental Setup
Reference beam (usually not necessary)
Probe beam

## Slide 22: Experimental Procedure
Plasma + LED (IPL)
LED (IL)
Plasma (IP)
Background (IBG)

## Slide 23
O3 absorption spectroscopy
  N2 emission – rotational T

## Slide 24
  Detector
  He + H2O
OH absorption spectroscopy

## Slide 25
Advanced techniques

## Slide 26
  Problem 1: No spatial resolution
  Solution: Abel transform of signal (for spherically symmetric plasmas)
Abel transform

## Slide 27
  Problem 2: Not enough signal
  Solution: Multipass cells for higher effective absorption length
  Cavity ringdown absorption spectroscopy
  Measurement of absorption coefficient through decay time
Cavity ringdown spectroscopy

## Slide 28
Thank you!
-
Questions?