## Slide 1: Plasma Diagnostic Techniques Lecture 2: Optical Emission Spectroscopy
Deborah O’Connell
York Plasma Institute

## Slide 2
The Bohr Model of the Atom
Nucleus
electrons
Electrons can only be in specific orbits around the central nucleus
These orbits have discrete energy states
Electrons in atoms and molecules can also be raised to higher energy states – electronically excited states

## Slide 3
Light Production - Excitation
One of the simplest ways to form excited states is to bombard atoms with energetic electrons
Usually excited states have short lifetimes (tens of nanoseconds) and decay – the electrons drop back to a lower energy state, eventually stopping at the lowest energy state – the ground state
Energy has to be given up in this process and this is normally through the emission of a photon
hν
Electron impact excitation:

## Slide 4
Electron velocity distribution functions

## Slide 5
Electron energy distribution function
Example: Druyvesteyn distribution
Notes: Comparison of a fit to data for a Maxwellian and Druyvesteyn distribution

## Slide 6
    line emission
      which emission lines (qualitative)
        species
      absolute intensities (calibration difficult)
        density of excited species
      line ratios
        robust model based analysis
      line shapes (high experimental requirements)
        temperatures, fields, densities
      temporal variations
        plasma dynamics
    continuum radiation
      spectral distributions
      absolute intensities
Optical Emission Spectroscopy (OES)

## Slide 7
Thomson scattering (top figure)
Laser induced fluorescence (bottom figure)
Interferometry
Photo-detachment
Absorption spectroscopy
Cavity ring down spectroscopy
Examples of active optical techniques

## Slide 8
Complete thermodynamic equilibrium (CTE)
    homogeneity
    unique temperature (Te = Ti = Tgas)
    black body radiation
    Maxwell-Boltzmann distribution describes the population of excited states for all components
    Practically not possible in the laboratory, thermal plasmas often modeled for simplicity
Plasma concepts - CTE

## Slide 9
Maxwell-Boltzmann distribution
  population distributions
    Spectroscopy: line intensities and ratios
  velocity distribution
    Spectroscopy: line shape, e.g. Doppler effect
Plasma concepts - CTE

## Slide 10
Main constraints and limitations
  inhomogeneities
  Planck
  Local thermodynamic equilibrium?
Plasma concepts - CTE

## Slide 11
Local thermodynamic equilibrium (LTE)
    local parameters
    collision dominated
        equilibrium of collisions
        no equilibrium of radiation
    requirement
    example (hydrogen arc)
      ne = 1016 cm-3, Te  104 K
        (Ek - Ei)LTE  4 eV
        Partial LTE
Plasma concepts - LTE

## Slide 12
Partial local thermodynamic equilibrium (PLTE)
    over population of the ground state
    LTE for excited states
    constraints and limitations
      low electron densities
  Corona model
  collisional radiative models
Plasma concepts - PLTE

## Slide 13
Corona model
model for plasmas with "low" electron densities (ne < 1013 cm-3)
applicable to most technological plasmas
far from thermodynamic equilibrium
most particles are in the ground state
electron impact excitation = relaxation by radiation
(spontaneous emission)
Plasma concepts - Corona