## Slide 1: Plasma Diagnostic Techniques Optical Emission Spectroscopy Lecture 6
Deborah O’Connell
York Plasma Institute

## Slide 2
Optical transitions: Spontaneous emission
Spontaneous emission
The discrete (line emission) energy Eik of the corresponding photon is directly related to the frequency nik (wavelength lik) of the emitted photon.
The number of emitted photons per unit volume and time:
is given by the product of the Einstein coefficient Aik and the population density ni in level i.
  The Einstein coefficient Aik describes the statistical (quantum-mechanics) optical transition probability for photon emission from a higher energy level i to a lower energy level k.

## Slide 3
Photon absorption
  The discrete (line emission) energy Eik of the corresponding photon is directly related to the frequency nik (wavelength lik) of the emitted photon.
Optical transitions: Photon absorption
The number of absorbed photons per unit volume and time:
is given by the the Einstein absorption probability coefficient Bki and the population density in in level k and energy density per unit frequency of electromagnetic radiation
  The Einstein coefficient Bki describes the transition probability for photon absorption from a lower energy level k to a higher energy level i.

## Slide 4
Stimulated emission
The discrete (line emission) energy Eik of the corresponding photon is directly related to the frequency nik (wavelength lik) of the emitted photon.
Optical transitions: Stimulated emission
The Einstein coefficient Bik describes the transition probability for photon transition induced by stimulated emission from a higher energy level i to a lower energy level k.
The number of emitted photons per unit volume and time:

## Slide 5
    So far we have been focussing on various plasma equilibrium models to analyse intensities of line emission from molecules, atoms or ions.
    With high-resolution spectrometers it is also possible to resolve and analyse the shape of emission (absorption) lines.
    This shape is influenced by various mechanisms and can contain very valuable information about plasma parameters, e.g. temperatures, densities, field strengths, etc.
Spectral line profiles - motivation

## Slide 6
    Thermal motion of the emitting particles along the direction of the observer causes Doppler shifts:
Line profiles – Doppler broadening
    For a Maxwellian velocity distribution function the spectral line shape of the photon flux F is given by a Gaussian profile:

## Slide 7
    The full width at half maximum (FWHM) is given by:
Line profiles – Doppler broadening
    This is a frequently used technique for temperature measurements.
    Non-isotropic shifts are very important in astrophysics to determine the movement of objects.

## Slide 8
    Energy spread in quantum states corresponds to frequency and wavelengths spread in line profiles:
Line profiles – energy, frequency, wavelength
    Be careful with the inverse correlation between frequency and wavelength! – non-linear

## Slide 9
    Heisenberg’s uncertainty principle:
Line profiles – natural broadening
    Natural lifetime of an excited state corresponds to a minimum energy uncertainty and associated line broadening.

## Slide 10
    The spectral line shape of the photon flux F in terms of energy is given by a Lorentzian profile around the energy E0 at the line centre:
Line profiles – natural broadening
    DE gives the width of the curve.
    Natural line broadening is typically the smallest broadening effect.

## Slide 11
    Collision induced pressure broadening is similar to natural broadening and occurs due to a collision induced reduction of the effective lifetime.
Line profiles – pressure broadening
kq : quenching coefficient with species Q
nq : density of species Q

## Slide 12
    Broadening can also be caused by electric microfields due to nearby ions.
    These microfields shift the quantum energy states by the Stark effect.
    The scaling of the effect on the spectral line profile is complex and non-monotonic – example see figure.
    It is an active research field and an often employed diagnostics for E-field and plasma density measurements.
    Similarly, broadening caused by the Zeeman effect is used for B-field measurements.
Line profiles – Stark broadening

## Slide 13
    Diagnostics based on line broadening can be very powerful, but different broadening effects typically contribute simultaneously.
    This requires a careful judgement of the investigated regime and appropriate de-convolution techniques.
    The convolution of different effects is generally iteratively given by:
Combination of broadening effects

## Slide 14
    The experimental profile of the spectrometer system can play a very important part in the overall profile.
De-convolution of broadening effects
    More typical are combinations of both in so called Voigt profiles. Extensive data bases exist for their analysis – see example in figure.
    Simple cases are combinations of Gaussian profiles only or Lorentzian profiles only:
(Gaussian profiles)
(Lorentzian profiles)

## Slide 15
Electromagnetic waves in plasmas
York Plasma Institute

## Slide 16
Radiative transfer

## Slide 17
Radiative transfer: example
    Reabsorption of emitted radiation can play an important part in radiative transfer – see illustration.
    An emitted photon is reabsorbed by a neighbouring atom and subsequently gets a ‘second chance’ to emit radiation through the same or a different transition.

## Slide 18
Radiative transfer: example
    Reabsorption can be included in the effective decay rate of excited states.
    Optically thin: gik=1
    Optically thick: gik=0

## Slide 19
The electromagnetic spectrum
http://en.wikibooks.org/wiki/Communication_Systems/Wave_Propagation