## Slide 1: Plasma Diagnostic Techniques Lecture 1
Deborah O’Connell
York Plasma Institute

## Slide 2: Aims & learning outcomes
Aims:
  Diagnostic techniques used to determine the properties of plasmas are examined. The physics behind particle and probe diagnostics, plasmas refractive index measurements, the spectroscopy of plasma emission from free and bound electrons, the scattering of electromagnetic radiation and fusion product detection are reviewed.
Learning outcomes - at the end of this module successful students will be able to understand:
  The underlying physics behind diagnostic techniques used in plasma research.
  Methods of measuring key plasma parameters from first principles.

## Slide 3: Overview
18 Lectures, including a lab ‘tour’
2 Practical classes
Coursework
  Two assignments, second half of the term
  15% of module mark
Closed exam
  1.5 hours
  85% of module mark

## Slide 4
Brief introduction to plasmas

## Slide 5: Temperature & density regimes

## Slide 6: Plasma research at the YPI

## Slide 7
Plasmas & other disciplines
Optics
Atomic & molecular physics
Laser physics
Surface sscience
Material science
Electro dynamics
Statistics
Numerical simulations
Electrical engineering
Chemistry
Bio-medical sciences

## Slide 8
What does a plasma consist of?
  ionised gas with variety of particles
  electrons
  positive and negative ions
  neutral particles (atoms, molecules, radicals)
  excited species
  dust particles
Parameters important to measure:
  densities
  distribution functions (temperatures)
  electric and magnetic fields
Plasma: complex multi-particle system

## Slide 9
What do we want to measure?
Particle densities (typically measured in particles / m3)
  Examples of particles include electrons, ions, and neutral reactive species
Temperatures (typically measured in eV, 1 eV = 11600 K or Kelvin)
  Electron temperaures, Te, are ‘hot’ and measured in eV
  Ions can be ‘cold‘ or ‘hot‘ (very dependent on plasma environment)
  Neutrals tend to be ‘cold‘ and measured in K
Species kinetics & dynamics (typically measured in seconds)
  Electron dynamics can be ‘fast‘ e.g. picoseconds
  Neutral chemical kinetics and surface processes are much slower
Typical quantities we want to measure:

## Slide 10
Multiphase interfaces:
  Plasma – gas – liquid – surface (solid)
Multispecies:
  Electrons, pos. ions, neg. ions, neutrals, radicals, excited species, photons
Multiscale problem – time:
  Electron dynamics: ps – ns
  Ion dynamics: 100 ns – μs
  Plasma chemistry: 100 μs – ms
  Surface chemistry: s – min
Multiscale problem – space:
  Surface structures: nm – μm
  Charged particle gradients: μm – m
  Neutral particle gradients: 10 μm – m
Plasma diagnostic challenges

## Slide 11
Overview of plasma diagnostic techniques
How do we measure plasma quantities and parameters?
Advantages and disadvantages
Complementary nature of multiple diagnostics & Combining diagnostics with simulations

## Slide 12
Electrical diagnostics
  charged particles and fields
    external current and voltage measurements
      simple
      non-intrusive
      indirect
      model based
      global information only
    probe measurements
      simple
      local information
      direct
      model based
      agressive environment (high temperatures or reactive gases)
      intrusive
Electrical techniques

## Slide 13
Ref: Marcus Alden, Lund University
Probe diagnostics
Can be intrusive
Example: Magnetron sputtering, time resolved measurements