## Slide 1: Plasma Diagnostic Techniques: Laser Induced Fluorescence (LIF/TALIF) spectroscopy
York Plasma Institute

## Slide 2
Emission spectroscopy
    passive
    simple
    robust
    indirect
    model based
    data needed
Laser spectroscopy
    direct
    highly reliable
    active
    involving
    expensive
Combination of passive and active methods
Optical diagnostics

## Slide 3: Detection of Atomic & Molecular Radicals by Laser Induced Fluorescence
Local measurement with high temporal resolution (ns) and very high detection sensitivity (provided background radiation is low).

## Slide 4
Diagnostic overview
to probe atomic oxygen
4
VUV absorption
  Absolute density
  Synchrotron  big facilities
  Vacuum environment  non realistic environment
Nanosecond TALIF
  Spatially resolved measurements
  Gas composition assumed  non realistic environment
  Calibration required  no direct absolute density
Picosecond TALIF
  Spatially resolved measurements
  No assumption on gas composition
  Calibration required  no direct absolute density
Niemi et al. – 2013 – APL 103 034102
Niemi et al. – 2005 – PSST 14 375

## Slide 5
Laser Induced Fluorescence
dependent on:
- density
-
- volume
- collection optics

## Slide 6
Two-photon Absorption Laser-Induced Fluorescence (TALIF)
   Ground state density deduced by measuring the fluorescence signal and lifetime of the excited state
laser excitation 2 x hν
hν
Ground state
Excited state
De-excited state
TALIF: principle

## Slide 7
Quenching
hν
hν
Natural lifetime
Quenching coefficient
Quench partner density
Effective lifetime
Effective decay rate
Effective lifetime
Effective decay rate
Natural lifetime
Quench partner density
Quenching coefficient
TALIF
Collisional quenching
Collision
hν
(remember lecture 3)
Collisional quenching of laser excited state

## Slide 8
TALIF: Why picosecond?
Example values:
8
Quenching coefficient:
Natural lifetime:

## Slide 9
Example: Technological applications incl. biomedical
  Atoms: Precursors
Determination of N, O & H densities
Atmospheric pressure low-temperature plasmas

## Slide 10
RF μAPPJ
MP1101 BIOPLASMA
Parameters | Typical values
Excitation | 13.56 MHz
Power discharge | 1-2 W
Feed gas | 1 slm He + 0-1 % O2 – N2/O2
Channel size | 1 x 1 x 30 mm3
Gas temperature | » 340 K
Electron density | » 1017 m-3
Electron temperature | » 3 eV
10
electrons
ions
radicals
neutrals
ions
ions
ions
h
h
energy
radicals
metastables
neutrals
metastables
Core plasma
Plume
Liquid
Biological sample

## Slide 11
Plasma plume characterization:
Atomic densities
Oxygen
Synthetic air

## Slide 12
Picosecond-TALIF:
Experimental set-up
Photodiode
Variable
attenuator
μAPPJ
on 3-axis translation stage
Picosecond laser system:
30 ps pulses @ 10 Hz
λ: 193-2300 nm
Narrow bandwidth
Laser energy
feedback
12
ICCD detector, sub-nanosecond resolution
Interference filter
Pre-trigger
Delay generator
Example species
O 225.58 nm
N 206.65 nm
H 205.08 nm

## Slide 13
laser excitation 2 x 225.62 nm
844.87 nm
Ionisation threshold
Photo-ionisation
1 x 225.62 nm
TALIF signal
E2Laser
Picosecond-TALIF:
Oxygen TALIF scheme
2p4 3P2,1,0
3p 3P1,2,0
3s 3S
13
40 μJ
Notes: Signal prop to sq of energy/intensity – 2 photon
Energy is per time

## Slide 14
Picosecond TALIF: Signal acquisition
Camera gate width = 2 ns
Delay step = 1 ns
14
Laser shot

## Slide 15
Picosecond TALIF: Extraction of parameters
relative density = S x A*
15

## Slide 16
Picosecond-TALIF:
Calibration schemes
844.87 nm
2p4 3P2,1,0
3p 3P1,2,0
3s 3S
2 x 225.65 nm
Oxygen
834.91 nm
5p6 1S0
6p'[3/2]2
6s'[1/2]1
2 x 224.31 nm
Xenon
16
Excitation at the same wavelength
 important to keep the laser properties identical
K. Niemi et al., Plasma Sources Sci. Technol. 14 (2005) 375-386

## Slide 17
Picosecond-TALIF:
Calibration schemes
17
Excitation at the same wavelength
 important to keep the laser properties identical
742-746 nm
2p3 4S3/2
3p 4S3/2
3s 4P1/2,3/2,5/2
2 x 206.65 nm
Nitrogen
656.3 nm
1s 2S1/2
3d 2D3/2,5/2
2p 2P1/2,3/2
2 x 205.08 nm
Hydrogen
826.3 nm
4p6 1S0
5p’[3/2]2
5s’[1/2]1
2 x 204.13 nm
Krypton

## Slide 18
Picosecond-TALIF:
Calibration set-up
ICCD detector, sub-nanosecond resolution
Interference filter
834 nm
Pre-trigger
Delay generator
Photodiode
Variable
attenuator
Picosecond laser system:
30 ps pulses @ 10 Hz
λ: 224.28 nm
Laser energy
feedback
Calibration cell
filled with Xe
18

## Slide 19
Picosecond TALIF: Pressure inside the cell
Compromise between signal and lifetime
Use the same camera gate width for both O & Xe
19
pXe = 10 Torr

## Slide 20
Picosecond TALIF: Calibration with xenon
T: transmission of the detection optics
η: detector’s quantum coefficient
σ: two-photon absorption cross section
hν: incident photon energy
Aik: Einstein coefficient
τ: effective lifetime
S: fluorescence signal
20
0.5% oxygen
pXe = 10 Torr
From literature
Measured

## Slide 21: Measured vs calculated decay rate
  Uncertainty in the calculated decay rate
     Error introduced in the density calculation
 For reliable density measurement, decay rate should be measured
Difference between measured & calculated
  Too large to be due to uncertainty of He quenching coefficient
  does not depend on admixture
 Might be induced by 3 body collisions with He

## Slide 22: Measured vs calculated decay rate
  Uncertainty in the calculated decay rate
     Error introduced in the density calculation
 For reliable density measurement, decay rate should be measured

## Slide 23
Comparison:
Synchrotron VUV absorption
Synthetic air admixture variation
Quantitative and qualitative agreement
Synthetic air  complex gas mixture
23
Niemi et al. – 2013 – APL 103 034102

## Slide 24
Plasma plume characterization:
Oxygen vs synthetic air
Oxygen
Synthetic air

## Slide 25
Plasma plume characterization:
Oxygen vs synthetic air
Oxygen
Synthetic air

## Slide 26
Thank you!