## Slide 1
Plasma Diagnostic Techniques:
Langmuir probe
York Plasma Institute
Presenter: Kari Niemi
Material: Jérôme Bredin
Academic: Deborah O’Connell
Notes: 1

## Slide 2
Historical Overview
Electrostatic probe diagnostic
Mott-Smith and Langmuir, Phys. Rev. (1926)

## Slide 3
Plasma
Electrodes
RF
I
LP
Isat.i
Isat.e
Vf
Vp
Expectation
Potential
Current
Reality
Vf
Vp
V
I
Electron saturation current
Ion saturation current
Principle
V
Rm
Floating potential
Plasma potential

## Slide 4
Vf
Vp
V
I
Collected electron current
For Maxwellian electron energy distribution:
Only electrons with energy E > Vp – V can reach the probe
Information on electrons energy distribution
A probe surface area
Γe collected electron flux
ne electron density
ve mean thermal electron velocity
Electron Collection Region

## Slide 5
Plasma requirements:
    weakly-ionized (non-thermal)
    plasma sheath collision-less for electrons (low-pressure)
    isotropic EED (non-magnetized plasma).
EEPF (eV-3/2cm-3)
Probe potential (V)
Collected current (A)
Electron Energy distribution

## Slide 6
Non-thermal EED
Low pressure
    Cold electrons trapped in the bulk
    Electrons above Vp depleted, since they can escape
High pressure
    Thermalization through e-e collisions
    Depletion above ionisation threshold (highly inelastic collisions)
V. Godyak and V. Demidov, J. Phys. D: Appl. Phys. (2011)
Maxwellian distribution
electrons in thermo-dynamical equilibrium
characterised by ‘one’ electron temperature (slope of EEPF)
Maxwellian
non-Maxwellian

## Slide 7
Vf
Vp
V
I
Plasma potential
Distance to centre
sheath
pre-sheath
plasma bulk
ni
ne
s
l
Langmuir probe tip
Ion Collection Region
Vp
0
wall
For non-planar probes, the ion collection area depends on the sheath width, which increases with the bias voltage, leading to a continuous increase in ion current (above the actual saturation value).
Notes: 7

## Slide 8
Vf
Vp
V
I
Planar probe
Guard ring
s
r
Ion Saturation Region
For a planar probe, the ion collection area is independent off the sheath width, which allows an independent calculation of the ion density.
Notes: 8

## Slide 9
Particularly in capacitively-coupled radio-frequency driven plasmas, the characteristic voltage potentials within the plasma bulk region oscillate substantially on the driving frequency.
M. Lieberman, A. Lichtenberg, John Wiley and Sons, New York (2005)
I
V
ϕP
t
Time averaged I-V probe curve yields ‘too high’ electron temperature
Plasma oscillations, RF plasmas

## Slide 10
Block potential oscillations on the driving frequency and its higher harmonics (due to non-linear nature of plasma sheath) by electrical filters in probe circuit.
Probe Compensation

## Slide 11
Pros
Instrumentation: Simple
Resolution: Local & not highly time-resolved
Method: Direct
Cons
Interpretation: Based on plasma sheath models
Diagnostic: Intrusive
Limitations: (1) harsh environments (damage), (2) complex chemistry (multi-species/electro-negative), (3) higher pressure environments (theory)
Summary

## Slide 12
Application
Plasma Propulsion with Electronegative GASES (PEGASES thruster)

## Slide 13
Application
Experiment requirements:
  Measurements ⊥ B
  Ra = 0.025 mm < RLe = 0.1 mm
Measurement:
  Tips : Platinum-Iridium
  Tip ⊥ B ⇒ measure
  Tip // B ⇒ reference
  No passive filter
l = 6 mm
∅ = 0.05 mm
∅ = 1.65 mm
∅ = 0.20 mm
∅ = 0.20 mm
⊥ B
// B

## Slide 14
Application
SF6 ion prod. rates
Without magnetic filter High Te ~ 5 eV suppresses formation of negative ions
With magnetic filter Lowered Te ~ 2eV enables formation of negative ions